## Slide 1: Candy 24 bits RISC-V style CPU Part 1: Register File
Zhiwei Luo & Qingruo Si
2018.11.28

## Slide 2: RISC-V
RISC-V is a free and open Instruction set architecture
Enables a new era of processor innovation through open standard collaboration.
Born in academia and research, RISC-V ISA delivers a new level of free, extensible software and hardware freedom on architecture, paving the way for the next 50 years of computing design and innovation.
cite: https://riscv.org/

## Slide 3: Systematic Overview

## Slide 4: Customized RISC-V ISA Specification
Inst | Function | type | TypeCode | Opcode
add | Add | R | 00 | 000000
addi | Add immediate | I | 01 | 0000
sub | Sub | R | 00 | 000001
mul | Mul | R | 00 | 000010
div | Div | R | 00 | 000011
divu | Div unsigned | R | 00 | 000100
rem | Rem | R | 00 | 000101
remu | Rem unsigned | R | 00 | 000110
and | And | R | 00 | 001000
andi | And immediate | I | 01 | 0001
or | Or | R | 00 | 001001
ori | Or immediate | I | 01 | 0010
xor | Xor | R | 00 | 001010
xori | Xor immediate | I | 01 | 0011
sll | Shift left | R | 00 | 010000
slli | Shift left immediate | I | 01 | 0100
sra | Shift right arithmetic | R | 00 | 010001
srai | Shift right arithmetic immediate | I | 01 | 0101
srl | Shift right | R | 00 | 010010
srli | Shift right immediate | I | 01 | 0110
slt | Set less than | R | 00 | 100000
slti | Set less than immediate | I | 01 | 0111
sltiu | Set less than immediate unsigned | I | 01 | 1000
beq | Branch if equal | SB | 10 | 0000
bge | Branch if >= | SB | 10 | 0001
bgeu | Branch if >= unsigned | SB | 10 | 0010
blt | Branch if < | SB | 10 | 0011
bltu | Branch if < unsigned | SB | 10 | 0100
bne | Branch if != | SB | 10 | 0101
jal | Jump and Link | UJ | 11 | 000
jalr | Jump and Link register | I | 01 | 1001
lb | Load byte | I | 01 | 1010
lw | Load word | I | 01 | 1011
lui | Load upper immediate | U | 11 | 101
lli | Load lower immediate | U | 11 | 100
sb | Store byte | S | 10 | 1000
sw | Store word | S | 10 | 1001
R(Register) | Typecode | Opcode | RS1 | RS2 | RD | 
I(immediate+Reg) | Typecode | Opcode | RS1 |  | RD | imm
S(Reg+Addr) | Typecode | Opcode | RS1 | RS2 |  | imm(addr)
SB(Branch) | Typecode | Opcode | RS1 | RS2 |  | imm
U(big imm) | Typecode | Opcode |  |  | RD | imm(big)
UJ(Jump addr) | Typecode | Opcode |  |  | RD | imm(addr)
Inst Coding | TypeCode(2b) | Opcode | RS1 | RS2 | RD | imm
R | 00 | 6b | 4b | 4b | 4b | 4b(unused)
I | 01 | 4b | 4b |  | 4b | 10b
S/SB | 10 | 4b | 4b | 4b |  | 10b
U/UJ | 11 | 2b |  |  | 4b | 16b
R | 14
I | 12
S/SB | 8
U/UJ | 3
Word | 24bit
Half-word | 16bit
Byte | 8bit

## Slide 5: Calling Convention
Register | ABI name | Description | Saver
R0 | zero | Hard-wired 0 | 
R1 | RA | Return Addr | caller
R2 | SP | Stack Pointer | callee
R3 | FP | Frame Pointer | callee
R4 | A0/RV | Arg0/Return value | callee
R5 | A1 | Arg1 | callee
R6 | A2 | Arg2 | callee
R7 | A3 | Arg3 | callee
R8 | S0 | Saved register | callee
R9 | S1 | Saved register | callee
R10 | S2 | Saved register | callee
R11 | S3 | Saved register | callee
R12 | T0 | Temporaries | caller
R13 | T1 | Temporaries | caller
R14 | T2 | Temporaries | caller
R15 | T3 | Temporaries | caller
PC | PC |  | 

## Slide 6: Register File
Read
Write

## Slide 7
ModelSim Simulation Result
R0:
Hard-wired zero

## Slide 8
ModelSim Simulation Result
write

## Slide 9
ModelSim Simulation Result
Read

## Slide 10
ModelSim Simulation Result
Reset

## Slide 11: Synthesis
Register file

## Slide 12
24 bits Register

## Slide 13
Layout after adding clock tree
Place and Route

## Slide 14
Layout after Routing

## Slide 15
Timing delay

## Slide 16
Summary
Area
Timing
Size & Power Report
Power
8780 nm
4,196,126.425 nW
2238 ps
2

## Slide 17
Question?